Category/Name/Description	Parameters	Comments/default
Main Input/Output
input:load current image to process (from Omero or Files)	project:name of project name / dataset:name of dataset name / image:name of the image / channel:the channel number / frame:the frame number	project:?project? / dataset: ?dataset? / image:?image? / channel:?channel? / frame:?frame? / Channel and frame number start at 1
output:save the current image (to Omero or Files)	project:name of project name / dataset:name of dataset name / image:name of the image	project:?project? / dataset:?dataset? / Will delete previous image with same name
Additional Input/Output
attach:attach a file to an image data (in Omero or Files)	project:name of project name / dataset:name of dataset name / image:name of the image data / dir:directory / file:filename to attach to the project/dataset/name image data	project:?project? / dataset: ?dataset? / image:?image? / Can use special directory names (?ij?,?home?,?tmp?
attachList:attach a list of files to an image data (in Omero or Files)	project:name of project name / dataset:name of dataset name / image:name of the image data / dir:directory / list:list of filenames to attach to the project/dataset/image image data	project:?project? / dataset: ?dataset? / image:?image? / Can use special directory names (?ij?,?home?,?tmp?
delete:delete a file	dir:directory / file:file name	(keywords for file) / (keywords for dir)
deleteList:delete a list of files	dir:directory to find files to delete / list:list of files names separated by ,	(keywords for file) / (keywords for dir)
inputBinning:input a binned data (reduce memory)	project:name of project name / dataset:name of dataset name / image:name of the image / channel:the channel number / frame:the frame number / binningXY:binning in XY / binningZ:binning in Z	project:?project? / dataset: ?dataset? / image:?image? / channel:?channel? / frame:?frame? / binningXY:1 / binningZ:1
load:load an image from file	dir:directory / file:file name(keywords for file) / (keywords for dir)	(keywords for file) / (keywords for dir)
loadOMERO:load a hyperstack image from OMERO / (use with caution)	project:name of project name / dataset:name of dataset name / image:name of the image / channels:the channels to load (c0-c1) / frames:the frames to load (t0-t1) / (you can use all to specify all channels or all frames)	project:?project? / dataset: ?dataset? / image:?image? / channels:1 / frames:1 / Channel and frame number start at 1
mergeChannels: merge color channels	dir:directory for the files to merge / list: list of files to merge / rgb: rgb mode (yes) or composite mode (no)	(keywords for dir) / (keywords for file) / rgb:no
noInput:to use when no specific input is required as first module	No parameters
save:save an image as a file	dir:directory / file:file name / format:file format to save	(keywords for file) / (keywords for dir) / format:tif by default, else can be zip
sequence: open a stack as sequence of 2D images	dir: directory containing the files / filename: pattern that file names should contain (or * for all files) / dimension: Z (or T)	(keywords for dir) / filename:* / dimension:Z
test:create a image with random noise	3D:creates 3D image	3D:no (will create a 2D image by default, use yes for a 3D image)
Calibration
calibrationLoadAndApply:will load a saved calibration and apply it to an image (current one by default). Will update calibration on OMERO.	dir:directory of the saved calibration / file:name of the saved calibration file / project:name of project name / dataset:name of dataset name / image:name of the image	project:?project? / dataset: ?dataset? / image:?image? / (keywords for file) / (keywords for dir)
calibrationSave:saves the calibration of the current image into a file	dir:directory of the saved calibration / file:name of the saved calibration file	(keywords for file) / (keywords for dir)
calibrationSet:will set the calibration to the current image	scaleXY:pixel size in XY / scaleZ:pixel size in Z	scaleXY:1 / scaleZ:1
Processing
crop:crop the image using a Roi	dir:directory of the roi / file:name of the roi file	Will use ImageJ roi file
cropZ:crop the image in the Z dimension	zMin:slice number for first z / zMax:slice number for last z	Slice numbering starts at 0
invert:invert gray values	No parameters
math:arithmetic operation between images	dir:directory for the other image / file: file name for the other image / operation:arithmetic operation to perform / coef0:coefficient to apply for first (current image) / coef1:coefficient to apply for second (other image)	coef0: 1 / coef1: 1 / The available operations are : add, mult, max, min and diff / A subtraction will be performed with add and coefficient -1
normalise:normalise intensity values	mean:new mean value / sd:new standard deviation value	mean:128 / sd:32
project:project in Z a 3D image	No parameters	Will perform maximum projection
scale:scale a image	scalex:the scale ratio in X / scaley:the scale ratio in Y / scalez:the scale ratio in Z / normalise:normalise the Z dimension (will override scalez)	scalex:1 / scaley:1 / scalez:1 / normalise:no (put “yes” to normalise)
Filtering
filters:filter an image (2D and 3D version)	radxy:the radius of filtering in X-Y / radz:the radius of filtering in Z / filter:the filter to apply	radxy:2 / radz:0 / Available filter parameter values are : median, mean, tophat, open, close, min and max
filtersCLIJ:filter an image (2D and 3D version) using CLIJ.	radxy:the radius of filtering in X-Y / radz:the radius of filtering in Z / filter:the filter to apply	radxy:2 / radz:0 / Available filter parameter values are : median, mean, tophat, open, close, min and max
rollingBall:applies the rolling ball algorithm from ImageJ (2D)	radius:radius of the rolling ball / dark:dark (yes) or light (no) background	radius:50 / dark:50
Threshold
autoThreshold:threshold an image using automatic threshold	method: the method to use (based on IJ automatic threshold) / dark:for dark background	method can be one of the following : Isodata, Otsu, Intermodes, Yen, Triangle, Mean, Huang, IJ_Isodata / dark is yes by default, set it to no for light background
threshold:threshold an image (creates binary image)	value:the thresholding value (for bright pixels)
percentileThreshold:perform thresholding based on percentage of brightest pixels	percentile:percentile value between 0 and 1 (for instance 0.05 will compute the threshold for 95% of the pixels, i.e 5% of the brightest pixels)
Threshold / Segment
hysteresis:perform a hysteresis threshloding	minValue:low threshold value / maxValue:high threshold value / labeling:also labels the image	Keep objects thresholded with low threshold but containing values with high threshold) / labeling:no (will create a binary image, set to yes to create a labelled image)
iterative:iterative thresholding, detect objects using multiple thresholds, based on compactness criteria	minVolume:minimum volume for objects / maxVolume:maximum volume for objects / minThreshold:minimum threshold	minVolume:100 / maxVolume: / -1 (no maximum limit) / minThreshold:0
label:label a binary image and detect individuals objects	minVolume:minimum volume for objects / maxVolume:maximum volume for objects / unit: yes if volume in unit, else in voxels	minVolume:0 / maxVolume: / -1 (no limit on max volume) / unit:no (voxels by default)
watershed:performs watershed segmentation	seedsRadius: radius in X-Y-Z to compute seeds (in pixels) / seedsThreshold:minimum value to be considered as seeds / signalThreshold:minimum value for signal	Will compute local maxima and use them as seeds for watershed
Post-processing / mathematical morphology
biggest:keep only the biggest object from labelled image	No parameters
closeLabels: performs closing on labelled objects	radxy:the radius of filtering in X-Y / radz:the radius of filtering in Z	radxy:5 / radz:0
excludeEdges:exclude labeled objects touching edges in XY and Z	excludeZ:exclude objects touching edges in Z	excludeZ:no (only exclude in XY by default)
fillHoles : fills holes in images using ImageJ algorithm (2D)	No parameters
filterObjects:filter objects in a labelled image	minValue:minimum value / maxValue:maximum value / descriptor:the descriptor to use for filtering (volume, compactness, elongation, compactnessDiscrete)	minValue:0 / maxValue:1 / Objects not within the defined range will be deleted from labelled image
separate2D:performs ImageJ binary watershed (to separate touching objects)	No parameters
Analysis / Measurement
analyzeParticles:performs the analyzeParticles function from ImageJ (labelling + measurements)	minSize:minimum size for particles / maxSize:maximum size for particles / unit:yes/no if size in unit / minCirc:minimum circularity / maxCirc:maximum circularity / excludeEdges:exclude particles touching image edges / list:list of measurement / dir:directory for results file / file:name for results file	minSize:0 / maxSize:-1(for no limit in size) / minCirc:0 / maxCirc:1 / list:area,perimeter (default), additional measurement are centroid, ellipse, shape and feret / file:results.csv
measurement:measurement to perform on labelled image	list:list of measurements to perform separated by comma / dir:directory to save results / file:file name to save results	(keywords for file) / (keywords for dir) / Available measurements for list : volume,area,centroid,compactness,ellipsoid,DC (Distance to Center)
multiColoc:quantify colocalisation between objects from two images	dirLabel:directory for the second image / fileLabel:file name for the second image / dir:directory for results file / file: file name for results file	(keywords for file) / (keywords for dir)
number:quantify objects inside other objects using another labelled image	dirLabel:directory for the second image / fileLabel:file name for the second image / dir:directory for results file / file: file name for results file	(keywords for file) / (keywords for dir) / The results will be saved as a .csv file / file:results.csv / Results will be volume occupied by objects and number of objects
quantif:signal quantification to perform on a labelled image	dirRaw:directory to the raw signal image / fileRaw:file name of the raw signal image / dir:directory to save results / file:file name to save results / list:list of quantification to perform separated by comma	(keywords for file) / (keywords for dir) / The results will be saved as a .csv file / file:results.csv / Available quantifications in list : mean,min,max,sd,sum,centre
Analysis / Distances
distancesBorder:compute distances center to center for all pairs of objects within the image	dir:directory for results file / file: file name for results file	(keywords for file) / (keywords for dir)
distancesBorder2:compute distances border to border for all pairs of objects in two images	dirLabel:directory for the second image / fileLabel:file name for the second image / dir:directory for results file / file: file name for results file	(keywords for file) / (keywords for dir)
distancesCenter:compute distances center to center for all pairs of objects within the image	dir:directory for results file / file: file name for results file	(keywords for file) / (keywords for dir)
distancesCenter2:compute distances center to center for all pairs of objects in two images	dirLabel:directory for the second image / fileLabel:file name for the second image / dir:directory for results file / file: file name for results file	(keywords for file) / (keywords for dir)
distancesCenterBorder2:compute distances center to border for all pairs of objects in two images	dirLabel:directory for the second image / fileLabel:file name for the second image / dir:directory for results file / file: file name for results file	(keywords for file) / (keywords for dir)
Analysis / Other
density:compute the density of objects based on neighbouring distance analysis	neighbours:numbers of neighbours to use for computation / radius:extension radius from each object	Neighbours:10
edt_evf:computes the euclidean distance transform (EDT) or the eroded volume fraction (EVF) as a normalised EDT	evf:computes EDT (no) or the EVF (yes)	evf:no (computes EDT by default) / EVF is computed per label
evfLayers:compute objects distribution within evf layers (layers with equal volumes)	dirEvf:directory for the evf image / fileEvf:file name of the evf image / nbLayers:number of layers / dir:directory for results image / file:file name for results image	(keywords for file) / (keywords for dir) / A csv file along with a png image file will be output. The -all files will serve as control and contains all evf values within a layer.
localThickness:computes calibrated local thickness (based on ImageJ localThickness plugin)	No parameters
Misc.
exe:execute a program (experimental feature)	dir: full path to the exe file / file: name of the exe file / arg: argument of the executable	(keywords for file) / (keywords for dir)
macro:run an ImageJ macro	dir:directory for macro / file: macro file name	(keywords for file) / (keywords for dir) / The macro should create a new image window as a result
show:display the current image	title:title for the image	title:?image? (name of the current image) / Will not display the image in batch mode.
sleep: pause execution	(sec)
subProcess:execute a TAPAS processing file	dir:directory of the processing text file / file: file name of the processing text file	(keywords for file) / (keywords for dir)
Utilities
appendResults:append a result table to another one	dir:directory for the files to process / file1:first file / file2:second file	(keywords for file) / (keywords for dir) / The file2 will be appended to file1
mergeResults:merges two or more results tables	dir:directory for the files to merge / list:list of file name to merge / fileMerge:file name of the merged file (will be saved in the same directory as input files)	(keywords for file) / (keywords for dir)

Specials keywords :
For the name of an image in Omero or a file name :
?project? : the name of the current project
?dataset? : the name of the current dataset
?image? : the name of the current image (?name? is deprecated from 0.6.3)
?channel? : the channel number of the current data
?channel+1? : the channel number +1 of the current data
?channel-1? : the channel number -1 of the current data
?frame? : the frame number of the current data
?frame+1? : the frame number +1 of the current data
?frame-1? : the frame number -1 of the current data

For a directory name :
?home? : the user home directory
?ij? : the ImageJ/Fiji directory
?tmp? : the system temporary directory